This is the procedure to change the Lamp Current Harness (Part#: D02-1013-080)

Using a 3/16” Allen Wrench loosen the two screws on the lamp housing assembly.

Remove the lamp housing, be sure not to lose any washers used as spacers.

Unplug the lamp connector from the lamp board.

Remove the four screws securing the source cover to the sensor.  Lift cover away from the sensor to remove.

Remove the three screws securing the shield to the board.

Remove the shield.

Loosen the two screws at the top of the board about ¼”.

Disconnect harness.

Gently pull board away from frame so you can pull harness out from behind the board.

Remove old harness and discard.  Install new harness.  Installation is reverse of removal.